The Siml Compiler
The Siml compiler translates a simulation program from the Siml language into the Python language. The translated program uses Numpy and Scipy for numerical computations.
Data Flattening and Code Collecting
The Siml language organizes a simulation in an object oriented tree structure. Algorithms are kept together with data for code reuse and encapsulation. Usual libraries for solving differential equations however, expect a completely different form: The state variables must be a one-dimensional vector of numbers. The system dynamics must be contained in a single function, which is called repeatedly during the solution process.
The Siml compiler converts the simulation program to the form which solvers need. This process is called 'data flattening' and 'code collecting' in this document.
The Simulation Object
In Siml a dynamic system consists of one (root) simulation object, that contains all data and algorithms. The object supports three special methods that are called by the solver:
'initial()' - called once at the beginning of the simulation, computes initial values.
'dynamic()' - called repeatedly during the solution process, computes the derivatives.
'final()' - called once at the end of the run, for displaying graphs.
The simulation program's code is restructured (collected) into these three functions. The conversion of the data into a one-dimensional vector is invisible to the user.
The generated Python object has an additional method to compute algebraic variables. Algebraic variables are ignored by the usual solvers, who only see the state variables.

---
The Siml Compiler
Object oriented
Built in (Float) objects as leaves
translation
Single
array
Float
d
b
a
sim1
c
foo(this, x:Real=0)
a = 2*x
b = a**2
System
dynamics
Solver

---
The SIML Language TODO
class foo(model):
data a: Float = 2
#Syntax for values with units needs to be determined
data s: Quantity unit(m) = 2 * unit(cm)
data s: Quantity [m] = 2 * [cm]
data v: Physical in [km/h] = 20[m/s]
data xEnd: Value in [mm]
#Syntax for distributions needs to be determined
data gr: Grid(nDim=1, dim0Unit=[mm])
data x: DistributionDomain(gr, 0)
data c: Distribution(grid=gr) in [g/l]
func dynamic():
#Syntax for boundary computation missing
c[0] = 2*[g/l]
boundary diff(c[xEnd], 0) == 0
#Syntax for access to differentials needs work
$s = v; s`= v; #These two seem interesting
s`time = v; s$time = v; diff(s, time) = v;
#for partial differentials
$c = D * diff(c, 0, 0) + q_chem
$c = D * c$0$0 + q_chem
c` = D * c`0`0 + q_chem; c`= D * c`x`x + q_chem
$c = D * c_0_0 + q_chem

---
Object Construction Semantics
The exact semantics of object construction have to be decided.
There are several alternatives:
Current semantics (mix of Python and prototype language)
Data and methods are defined in class body. (important)
At instance construction only the data attributes are copied to the instance. (strange)
The '__init__' method is called directly after construction with constructor arguments.
Data attributes are looked up in the instance.
Methods are looked up in the class. (strange, like Python)
Methods are wrapped in 'bound methods' when they are accessed.
Easy to call methods of a base class: Base.method(this, a, b, c) (important)
More prototype like semantics:
Data and functions are defined in class body. (important)
At instance construction all attributes are copied to the instance.
Do methods need to be wrapped in bound methods? (strange)
How are methods of the base class called? (read up on prototype languages)
Classes are really special factory functions (old class model)
Inheritance is difficult if there are constructor arguments. Class templates in C++ are similar.(strange)
No other language as an example, except for overly complicated C++. (strange)
Python semantics:
Methods are defined in class body, data is defined in '__init__' function. (inconvenient)
C++ semantics:
Data and methods are defined in class body. (important)
Constructors of data attributes have to be called in the instance's constructor. (very bad)

---
Overview
From Siml to Python
Parser: Parse the program text -> AST
Interpreter: Execute AST -> Interpreter objects (symbol table), compiled AST
Compute constants
Set up objects
Create data tree of compiled object (part of symbol table)
Collect collect statements of main functions (compile AST)
Flatten data tree.
Optimizer:
Create data flow decorations
Check data usage errors
Reorder statements
Optimize
Remove variables that are used only once
Algebraic simplification of expressions
Attempting to find closed solutions to partial problems
Code Generator: Generate Code -> Python (C in distant future)

---
The Parser
The parser creates the AST

---
The Interpreter

---
Interpreting the AST
The Abstract Syntax Tree (AST) is created by the parser from the program's text. The AST is interpreted in a similar fashion like Python interprets a module. Special 'compile' statements create compiled code.
Values can be known or unknown at compile time. The interpreter can handle unevaluated expressions. All statements on module level must operate on values, that are known at compile time (constants). Only code that is called by the compile statement, can operate on variables.
For every file a 'module' with an own namespace is created.
The module is the global namespace of the interpreter.
'class' statements create class objects in the module.
'func' statements create function objects.
'data' statements create class instances (variables).
'compile' statements create Python code.
Initialize the collection infrastructure for unevaluated code.
Initialize infrastructure for data flattening
Call top level simulation functions ('initialize', 'dynamic', 'final'), and collect unevaluated code.
Send simulation object to code generator
Assignment ('=') statements call the __assign__ method of the class.
Expression statements (function calls) are executed, the return value is discarded.

---
AST
Structure of the Abstract Syntax Tree (AST)
Program
The AST is created by the parser. It represents the program's text.
Global constant
Float
g
Class definition
Data statement: Define class attributes and their type.
Foo
Float
a,b
foo(this, x:Real=0)
Method definition: Argument types and initial values are optional.
a = 2*x
b = a**2
Bar
Statements in function body.
Foo
c
Float
d
c.a = 5;
Data statement: Define global constant
myBar
Bar
Compile statement: Tell interpreter to create Python code.
sim1
Bar

---
Symbol Table – Root Namespace
root
Name Space Methods
has_attr()
get_attr()
set_attr()
del_attr()?
builtin
Float
__main__
Float
g
Float implementation
Foo
Implementation
not shown
Type subsystem:
is instance
Bar
myBar
Only built in (Float) objects as leaves
sim1
Bar
Foo
c
a
b
foo(this, x:Real=0)
a = 2*x
b = a**2
d

---
ExecutionEnvironment - Scope
Namespace
attributes
Namespace
Local Scope
This Scope
Global Scope

---
Callable Objects
Protocol
Inherit from interpreter.CallableObject
Have Python method __call__(self, *args, **kwargs) which executes the function's code.
The __call__ method
Siml objects (InterpreterObject, ast.Node) are passed as arguments.
The arguments may be unknown values or unknown expressions.
If function can not handle unknowns, it must raise UnknownArgumentsException (the interpreter then generates an unknown Expression)
For wrong argument types a IncompatibleTypeError is raised
Return values must be InterpreterObject or ast.Node
Arguments are parsed with the interpreter.Argument class.
The class works with positional and keyword arguments; it does type checking if types are given.

---
Zoo of Directly Callable Objects
Different types of directly callable objects
User defined (Siml) function:
Parse arguments and check argument types.
Executes code in Siml language.
Built in function wrapper:
Parse arguments and check argument types.
Call Python function
Raise UnknownArgumentsException if function can not handle unknown arguments.
Return unevaluated function call otherwise.
Method wrapper
Call wrapped function with 'this' as first positional argument
Special objects, for example: print function

---
Function Call Details

---
Assemble Program Tree
Parse tree from main source file:
Complete parse tree of whole program:
Set default data roles.
Interpret top level statements.?
Program
standard library
Real
resolve imports
recursively
Program
Real
= 3.1415;
pi
from stdlib import *
Bar1
Bar1
Flatten compound data definitions.
Real
a
Real
a,b
Real
b
a = 2;
a = 2;
Build symbol table?
Check semantic?
duplicate (inherited) symbols
assignments to constants
access to attributes
Bar2 (Bar1)
Bar2 (Bar1)
Foo
c
Foo
c
Real
d
Real
d
c.a = 5;
c.a = 5;
Build a recursive tree of data definitions. The leaves must be built in types.
See following slides
myBar2
Bar2
Build recursive data tree. Build function call tree, starting from main functions:
“init”, “dynamic”, “final”
compile Bar2;
Outdated! Design has changed!

---
Build Recursive Data Tree
3
Build tree
recursive
1.1
copy
2.1
copy
c
d
Foo
Real
c.a = 5;
a
b
Real
Real
a = 2;
interpret statements
1.2
myBar2
Bar2
2.2
interpret statements
Program
Foo
a
b
pi
Real
Real
Real
Real
Bar1
a
b
Real
Real
Bar2 (Bar1)
c
d
Foo
Real
c.a = 5;
a = 2;
0
= 3.1415;
myBar2
Bar2
c
d
Foo
Real
a
b
Real
Real
Real
Real
Real
Foo
a
b
Real
Real
= 2;
= 5;
Attach values to constants.
(Could also be done after flattening.)
4
Tree for one object.
out_Bar2
Bar2 (Bar1)
Outdated! Design has changed!

---
Collect Inherited Attributes
Create an augmented AST where each object contains all inherited data and all inherited methods???
Terminology for multiple methods with the same name:
Overloading: Different methods are selected based on type and number of parameters.
Overriding: Other methods of the same name become invisible.
Collect inherited data.
Data can not be overloaded or overridden: Giving a data attribute the same name like an inherited attribute is an error. (The error is shown in the child class.)
Collect inherited methods.
Methods can be overridden: When a parent class and a child class use the same name for a method, the parent class' method becomes invisible and must be called with the full name.
Overloading (method selection based on different argument types) (like C++ or Java) are future extensions.
Creation of “this” argument. Adding correct type specifier for future extension.
Intelligent clustering of data may give the ability to keep non static functions separate. (Contrary to inlining every function which is straight forward with flattening)
Outdated! Design has changed!

---
Collect Attributes of Submodels Recursively

---
The Flattening Process
Flatten the tree structure
Inline all code, and make it use the right data.
Collect global data and functions.
Create instances of all entities.

---
Flattening Data

---
Flattening Functions

---
“if” Statement Semantics
Algorithm for entering clauses and generating code:
If the condition evaluates to False at compile time: do not enter clause, no code will be generated for clause.
If the condition can not be decided at compile time (it contains variables or parameters): enter clause and generate code.
If the condition evaluates to True at compile time: enter clause, generate code, don't enter any further clauses. An 'else:' clause is equivalent to an 'elif True:' clause.
Special optimization:
“if” statements that are completely decidable at compile time are optimized away. This is the case if the compiler has entered only one clause. Then the compiler inserts the statements of the single clause into the program and removes the if statement entirely.
'return' statements are illegal inside 'if' statements. (To keep generated code simple.)
if a<1:
b = 2
else:
c = 3
if a<1:
b = 2
c = nan
else:
c = 3
b = nan
Compiler inserts
statements
Requirements for single/guaranteed assignment and statement reordering:
The last condition must evaluate to True at compile time (equivalent to 'else:', catch all clause).
All clauses of the 'if' statement must assign to the same variables. If a clause contains fewer assignments, the compiler creates the missing assignments automatically and inserts them into the clause.

---
Partial Differential Equations

---
Reordering Equations
Without equation reordering it is necessary to call all code from the main function. With reordering it is possible to call functions in lower level objects implicitly, which will result in much more beautiful code (but with harder to understand details).

---
More
Partition data into state vector, differential (return) vector, and other data; that stays constant during the simulation (parameters, constants).
Automatic differentiation, for higher solution speeds and for optimizers.
http://en.wikipedia.org/wiki/Automatic_differentiation
http://justindomke.wordpress.com/
ADOL-C: http://www.math.tu-dresden.de/~adol-c/ automatic differentiation for large systems.
Python bindings for ADOL-C: http://github.com/b45ch1/pyadolc/tree/master

---
Storing Simulation Results
Meta data for attributes:
A list of these objects needs to be contained in the result storage object.
AttributeDescriptor:
name = 'x'
unit = 'm/s'
slice = slice(3, 4) #Describes what part of the state/data vector are occupied by the variable
grid = ??? #On what grid is the distributed variable placed.
Parameter = ??? #additional information to identify parameters.
Protocol for storage class:
get_attribute(string()) → array() #return the time course of one variable
add_step_vars(array()) #add the variables of one time step to the storage.
save(filename)
load(filename)
init_attribute_types([AttributeDescriptor()]) ??? #There must be some way to tell the storage object how the data vector is structured internally.
set_param(string(), float()) #there must be a way to put the parameter values into the storage object.