The SIML Language
class foo(model):
{
data a: Real = 2;
#Syntax for values with units needs to be determined
data b: Quantity unit(m) = 2 * unit(cm);
data b: Quantity [m] = 2 * [cm];
data v: Physical in [km/h] = 20[m/s];
#Syntax for distributions needs to be determined
data gr: Grid(nDim=1, dim0Unit=[mm]);
data xEnd: Value in [mm];
data c: Distribution(grid=gr) in [g/l];
func dynamic():
{
#Syntax for boundary computation missing
c[0] = 2*[g/l];
boundary diff(c[xEnd], 0) == 0;
}
}

---
The Intermediate Language

---
The Generated Program

---
Overview: From Parse Tree to Intermediate Language
The Siml language organizes a simulation in a tree structure. The output of the compilation must be a program with a flat vector of numbers, because the usual integration software is structured this way.
The situation is similar for the methods ans functions. The integration software wants one function, which computes the time derivatives of the state variables. During the integration process it calls this function repeatedly. The Siml language uses two additional functions one called before the integration process, and one called after the integration process.

---
Parse Tree Modification
Expand compound data definitions.
Link all class definitions with their base classes.
Find undefined base classes.
Find cyclic base classes.

---
Program Tree
The initial base class 'object' is left out.
Only data is shown, functions are handled similarly.
Program
Built in class
Real
Standard Library
Real
= 3.1415;
pi
Global constant
User defined class
Foo
Compound data statement
Real
a,b
Bar1
Real
a
Real
b
Assignment to constant. Code in class body will be interpreted at compile time.
a = 2;
Bar2 (Bar1)
Foo
c
Real
d
c.a = 5;
Create a recursive tree of data definitions, so that all leaves are base types. Compile statements are handled similarly.
myBar2
Bar2
inheritance

---
Name Space Implementation
Name Space Methods
hasAttr()
getAttr()
setAttr()
delAttr()?
findDotName()
Real
pi
class
definition
Namespace
attributes
Real
a
Real
b
Real
c
f()
class
instance
data z: Foo
Foo
Namespace
attributes
Real
a
Real
b
Real
c
f()
Namespace
attributes
Module
class Foo

---
ExecutionEnvironment - Scope
Namespace
attributes
Namespace
attributes
thisScope
globalScope

---
Assemble Program Tree
Parse tree from main source file:
Complete parse tree of whole program:
Set default data roles.
Interpret top level statements.?
Program
standard library
Real
resolve imports
recursively
Program
Real
= 3.1415;
pi
from stdlib import *
Bar1
Bar1
Flatten compound data definitions.
Real
a
Real
a,b
Real
b
a = 2;
a = 2;
Build symbol table?
Check semantic?
duplicate (inherited) symbols
assignments to constants
access to attributes
Bar2 (Bar1)
Bar2 (Bar1)
Foo
c
Foo
c
Real
d
Real
d
c.a = 5;
c.a = 5;
Build a recursive tree of data definitions. The leaves must be built in types.
See following slides
myBar2
Bar2
Build recursive data tree. Build function call tree, starting from main functions:
“init”, “dynamic”, “final”
compile Bar2;

---
Build Recursive Data Tree
3
Build tree
recursive
1.1
copy
2.1
copy
c
d
Foo
Real
c.a = 5;
a
b
Real
Real
a = 2;
interpret statements
1.2
myBar2
Bar2
2.2
interpret statements
Program
Foo
a
b
pi
Real
Real
Real
Real
Bar1
a
b
Real
Real
Bar2 (Bar1)
c
d
Foo
Real
c.a = 5;
a = 2;
0
= 3.1415;
myBar2
Bar2
c
d
Foo
Real
a
b
Real
Real
Real
Real
Real
Foo
a
b
Real
Real
= 2;
= 5;
Attach values to constants.
(Could also be done after flattening.)
4
Tree for one object.
out_Bar2
Bar2 (Bar1)

---
Collect Inherited Attributes
Create an augmented AST where each object contains all inherited data and all inherited methods???
Terminology for multiple methods with the same name:
Overloading: Different methods are selected based on type and number of parameters.
Overriding: Other methods of the same name become invisible.
Collect inherited data.
Data can not be overloaded or overridden: Giving a data attribute the same name like an inherited attribute is an error. (The error is shown in the child class.)
Collect inherited methods.
Methods can be overridden: When a parent class and a child class use the same name for a method, the parent class' method becomes invisible and must be called with the full name.
Overloading (method selection based on different argument types) (like C++ or Java) are future extensions.
Creation of “this” argument. Adding correct type specifier for future extension.
Intelligent clustering of data may give the ability to keep non static functions separate. (Contrary to inlining every function which is straight forward with flattening)

---
Collect Attributes of Submodels Recursively

---
The Flattening Process
Flatten the tree structure
Inline all code, and make it use the right data.
Collect global data and functions.
Create instances of all entities.

---
Flattening Data

---
Flattening Functions

---
Computing Constants
Partial Differential Equations
Special handling of constant setup code. (separate function?)

---
Reordering Equations
Without equation reordering it is necessary to call all code from the main function. With reordering it is possible to call functions in lower level objects implicitly, which will result in much more beautiful code (but with harder to understand details).

---
More
Partition data into state vector, differential (return) vector, and other data; that stays constant during the simulation (parameters, constants).